## Slide 1: Leonard Design
Rev 13
11/5/2022

## Slide 2: Command Structure
UR
Sherlock
Gocator
Client
HALCON
LEonard
Cognex
Device Interface
⇒ System-specific Command String
OR
⇒ System-specific Command String
⇐ LeonardMessage
OR
⇐ LeonardMessage
Client Interface
⇒ LEonardMessage
OR
⇒ LEonardMessage
⇐ System-specific Response
OR
⇒ LEonardMessage
⇐ LEonardMessage (if client can parse)
LEonardMessage
<TERM> Message Terminator
default = <LF>
<DEL> Multistatement Statement delimiter
default = #
LEonardStatement<TERM> OR
LEonardStatement<DEL>LEonardStatement]<TERM
LEonardStatement
filename.py
filename.js
LE:LEonardStatement
JE:JavaScript
PE:PythonScript
varName=value
SET varName value
GET varName

## Slide 3: Variables
LEScript, Java, and Python have independent variables
LEVariables are variables created in LEScript
  All LEVariables are duplicated to Java and Python
  LEVariables are all strings
  A Java or Python variable can be written back to LEVariables
    leWriteVar(‘name’, value)
There are some special system LEVariables
  DateTime: Current yyyy-MM-ddTHH-mm-ss
  LEScriptFilename: currently executing LEScript program
  LEonardLanguage: Current language executing in LEScript
  LEonardRoot: Folder for the LEonard directory “tree”

## Slide 4: Program and Language Flow
LEonardRecipe
LEScript
LEScript
…
call(label1)
…
exec_java(JavaProgram.js)
…
exec_python(PythonProgram.py)
…
end
label1:
LEScript
LEScript
…
ret()
leLanguage(1)
Java Statements
leLanguage(2)
Python Statements
LEonardLib for all 3 Languages
labelname:
jump(label)
jumpif(condition, label) (LEScript has jump_gt_zero)
call(label)
callif(condition, label)
ret()
end()
lePrint(message)
leShowConsole(False | True)
leClearConsole()
lePrompt(message)
leExec(LEonardScript Line)
leSend(devName, message)
leAsk(devName, message, timeoutMs)
leLogInfo(message)
leLogError(message)
leClearVariables()
leWriteVar(varName, value)
leWriteVarSys(varName, value)
leReadVar(varName)
leLanguage(int language)
UseLEScript()
UseJava()
UsePython()
JavaProgram.js
Java Statements…
LEonardLib Calls
Java Statements…
PythonProgram.py
Python Statements…
LEonardLib Calls
Python Statements…
…

## Slide 5: Other LEScript Functions
LEScript: General
leLanguage(0|1|2)
exec_java(filename)
exec_python(filename)
clear()
import(filename)
var_name = 12.3 var_name = {other_var_name}
var_name++ var_name--
var_name -= 17.5 var_name += 18
label:
jump(label) jump_gt_zero(var_name, label)
call(label) return
prompt(message) sleep(seconds)
assert(var_name, value)
end
connect(device_name)
connect_all()
disconnect(device_name)
disconnect_all()
LEScript: Robot
save_position(name)
move_linear(name)
move_joint(name)
move_relative(dx,dy)
move_tool_home()
move_tool_mount()
free_drive(on/off)
set_linear_speed(speed_mm/s)
set_linear_accel(accel_mm/s^2)
set_joint_speed(speed_deg/s)
set_joint_accel(accel_deg/s^2)
set_blend_radius(blend_radius_mm)
select_tool(tool_name) set_part_geometry(FLAT|CYLINDER|SPHERE, part_diam_mm)
LEScript: Gocator
gocator_send(message)
gocator_trigger(pre_delay)
gocator_adjust()
write_gocator_data()
LEScript: Grind
grind_line(dx_mm, dy_mm, n_cycles, speed_mm/s, force_N, stay_in_contact)
grind_line_deg(length_mm, angle_deg, n_cycles, speed_mm/s, force_N, stay_in_contact)
grind_rect(dx_mm, dy_mm, n_cycles, speed_mm/s, force_N, stay_in_contact)
grind_serp(dx_mm, dy_mm, n_xsteps, n_ysteps, n_cycles, speed_mm/s, force_N, stay_in_contact)
grind_poly(circle_diam_mm, n_sides, n_cycles, speed_mm/s, force_N, stay_in_contact)
grind_circle(circle_diam_mm, n_cycles, speed_mm/s, force_N, stay_in_contact)
grind_spiral(circle1_diam_mm, grind_circle2_diam_mm, n_spirals, n_cycles, speed_mm/s, force_N, stay_in_contact)
grind_retract()
grind_contact_enable(0=Touch OFF,Grind OFF|1=Touch ON,Grind OFF| 2=Touch ON,Grind ON)
select_tool(tool_name) set_part_geometry(FLAT|CYLINDER|SPHERE, part_diam_mm)